## Slide 1: An Experimental Investigation of SIMO, MIMO,Interference-alignment (IA) and Coordinated Multi-Point (CoMP)”
Per Zetterberg and Nima N. Moghadam
INTERNATIONAL CONFERENCE ON SYSTEMS, SIGNALS AND IMAGE PROCESSING (IWSSIP)

## Slide 2: The USRP-based testbed: synchronization
GPS receiver
Output: 1PPS
NMEA (RS232)
On 50Ω cable
Output: 1PPS (50Ω)
NMEA: USB
USB splitter
10MHz ref.
To PC

## Slide 3: RF-hardware: TX
USRP2 / N210
XCVR2450
Mini-circuits ZHL 1724HLN
2.49GHz

## Slide 4: RF-hardware: RX
USRP2 / N210
Amplifier
Mixer
70MHz

## Slide 5: The testbed
3BS
10m
10m
3MS
P=15dBm
NF=10-11dB

## Slide 6
The 4Multi Software FrameWork
(Multi-Antenna, Multi-User, Multi-Cell, Multi-Band)
Send data in small bursts (relaxes computational load)
Nodes synchronized by external trigering (PPS)
The implementor (basically) only need to program three functions
node::init, node::process and node::end_of_run.
Simulate the system using “simulate” generic function.
Everything that can be compiled with gcc can run (e.g IT++)
Toolbox with coding&modulation.
Store _all_ received signals for post-processing.
Vision:
“The coding should be as easy as performing ordinary
(but detailed) desktop simulations”

## Slide 7: Software
UHD driver
four_multi
boost
ethernet
kernel
OFDM1
AMC
IA_node
calculate_
beamformers
IT++
USRP
PPS
10MHz

## Slide 8: Implementation IA
BS 1
BS 2
BS 3
MS 1
MS 2
MS 3
Feedback:
Wired ethernet

## Slide 9: Implementation: CoMP
BS 1
BS 2
BS 3
MS 1
MS 2
MS 3
Feedback:
Wired ethernet

## Slide 10: Beamformer
“Approaching the Capacity of Wireless Networks through Distributed Interference Alignment", by Krishna Gomadam, Viveck R. Cadambe and Syed A. Jafar.
Formulate virtual uplink SINR. Iterate

## Slide 11: Frames
Payload
10 OFDM symbols
Payload
10 OFDM symbols
CSI reference
signals
Demodulation reference signals
38 subcarriers,
312.5kHz carrier-spacing
QPSK, …., 256QAM
0.25, 0.5, 0.75 –rate LDPC codes
MS feed-back CSI to BS1.
BS1 calculate beam-formers.
BS1 sends weights to BS2, BS3.
BS1-BS3 frequency locked.

## Slide 12: Measurement Campaign
3BS + 3MS
Measurement divided into 116 batches.
Each batch 5 frames for IA, CoMP, MIMO, SIMO
MS moved several wavelengths between each batch.

## Slide 13: Results
16QAM, 0.75 rate coded.
.
 | All-data |  | Best BS |  |  | 
Method | FER | C-FER | FER | C-FER | Rate | C-rate
IA | 0.31 | 0.04 | 0.21 | 0.02 | 2.36 | 2.95
CoMP | 0.01 | 0.00 | 0.01 | 0.00 | 2.98 | 2.99
TDMA-MIMO | 0.08 | 0.01 | 0.04 | 0.00 | 1.93 | 2.00
TDMA-SIMO | 0.00 | 0.00 | 0.00 | 0.00 | 1.00 | 1.00
All-MIMO | 0.99 | 0.92 | 0.98 | 0.87 | 0.13 | 0.78
All-SIMO | 0.76 | 0.55 | 0.61 | 0.31 | 1.18 | 2.07

## Slide 14: How far from ideal ?

## Slide 15: SINRD per sub-carrier: IA

## Slide 16: SINRD per sub-carrier: CoMP

## Slide 17: Average over subcarriers

## Slide 18: Ideal versus actual
IA
CoMP
Ideal
Actual
Actual
Ideal

## Slide 19
Power-Amplifier Non-linearity
OFDM signals:
+
n
y+n(t)
Modeled as noise:
D Dardari, V. Tralli, A Vaccari “A theoretical characterization of nonlinear distortion effects in OFDM systems“, IEEE Trans. Comm., Oct 2000.

## Slide 20: Phase-noise
A/D
LPF
BPF
LNA
y(t)
Modeled as additive noise + CPE
CPE: Slowly varying between symbols
R. Corvaja, E. Costa, and S. Pupolin, “M-QAM-OFDM system performance in the presence of a nonlinear amplifier and phase noise, IEEE Trans. Comm. 2002.

## Slide 21: RF-impairment model
+
+
+
+
CPE =0.6deg
34dB below signal
40dB below signal

## Slide 22: Closing the gap: IA
Ideal
Actual
Model

## Slide 23: Closing the gap: CoMP
Ideal
Model
Actual

## Slide 24: Closing the gap TDMA-SIMO
Ideal
Model
Actual

## Slide 25: Closing the gap TDMA-MIMO
Ideal
Model
Actual

## Slide 26: Actual SINRD versus Path-loss ratio
Path-loss ratio
Path-loss ratio
SINRD
SINRD
IA
CoMP

## Slide 27: Conclusion
CoMP and IA implemented on a wireless test-bed.
Both IA and CoMP perform better than reference schemes SIMO and MIMO.
CoMP provides best performance.
Small hardware impairments degrade performance significantly in particular CoMP.
Impairment model proposed - fair agrement with measurements => test on more complex scenarios.
Hardware characterization can be improved.

## Slide 28: Next step
Implement adaptive modulation and coding.
More streams in CoMP.
Model hardware with detailed AM/AM, AM/PM and phase-noise spectrums.

## Slide 29: Radios
XCVR2450
Dual-band TRX 2.4GHz,5GHz
Tx power: 4 dBm (nice and linear)
RX NF: 20dB
Home-brewed receiver:
0.2-3GHz. NF: 10dB.
Ramin Fardi – design.
5GHz TRX. Goal: much better than XCVR2450. First testing just started.